## Slide 1: OPERATIOAL REQUIREMENNT OF BOREWELL RESCUE
Presented by:- Sohel Lakhani, DC

## Slide 2
OBJECTIVE
Upon completion of this lesson, you will be able to Describe:-
What is a Bore well.
Classification of Bore well.
Assessment and planning.
Bore well-Death Trap
Rescue Methods/Techniques
Equipment/ Improvised Equipment

## Slide 3: BORE WELL
Low yielding groundwater sources are found relatively close to the surface, usually under 30 m (100 ft).
Drilled using a rotary bucket auger.
Casing is perforated or uses a sand screen with continuous slot openings

## Slide 4: BORE WELL
Advantage: Large Diameter Casing (450-900 mm): Provides water storage for peak demand
Disadvantage:
a)Shallow Groundwater Aquifer: Can lead to depletion.
b)Water Shortages: Occurs after long dry spells.
c)Susceptible to Contamination: Vulnerable to surface land-use activities

## Slide 5: ASSESSMENT AND PLANNING
Initial Site Survey: Assess depth, diameter, condition of the borewell, and location of the victim.
Victim Monitoring: Use cameras and sensors to monitor the trapped individual’s condition and position.
Rescue Strategy: Decide between vertical retrieval (through same borewell) or parallel shaft drilling, based on borewell stability and victim’s depth.

## Slide 6: CLASSIFICATION OF BOREWELL
High Capacity Bore Well (HCB):
Casing Diameter: 10 or 12 inches.
Depth: >80 meters.
Design Yield: 20,000 GPH to 45,000 GPH.
Medium Capacity Bore Well (MCB):
Casing Diameter: 8 inches.
Depth: >80 meters.
Design Yield: 10,000 GPH to 20,000 GPH.

## Slide 7
Low Capacity Bore Well (LCB):
Casing Diameter: 6 inches.
Depth: 30m to 50m.
Design Yield: 1,500 gph to 5,000 gph.
Cont..

## Slide 8: BOREWELL DEATH TRAP
Unused Bore well are kept open
Children of different age went around due to curiosity
Children falling in the bore well.
Confined space
Hypoxia, unavailability of water
and food

## Slide 9: RESCUE METHOD/TECHNIQUES
No scientific or reliable method is available.
Manual rescue method: A large hole is dug beside the bore well to reach the child.
Requires heavy machinery (tractors, JCBs) and human resources.
Delays in mobilizing resources reduce chances of saving the child.

## Slide 10
If there’s a rock at depth, the entire process may need to be restarted, further delaying rescue.
The deeper the child is, the more complex and time-consuming the process.
Cameras are used for deeper rescues; parallel and horizontal bore holes are dug, but success is not guaranteed.
Cont..

## Slide 11
Estimating the type and size of rocks blocking the child’s location is difficult even with advanced geophysical tools.
Drilling through rock may cause the entire bore well to collapse.
Cont..

## Slide 12: TECHNIQUES ADOPTED BY NDRF
Rope Rescue
Magic ball
Umbrella Tool
Cloth bucket
Pendant jhula
Iron Rod in “L/J” shape
Cameras (with LED Light along with minimum 100 ft. wire and display)

## Slide 13: LIST OF MINIMUM ITEMS FOR BOREWELL RESCUE
Life Detector Type-I & II
Victim location equipment and Breaching System
Video Camera with Accessories
Thermal Imaging Camera
Inflatable Lighting Tower
Portable Generator 5.5 KVA

## Slide 14
Portable Generator 2.2 KVA
Rope Rescue
Magic Ball
Umbrella Tool
Cloth Bucket
Cameras (with LED Light along with minimum 100 ft. Wire and display)
Cont..

## Slide 15
Pendant Jhula
“L, J & U” T
Aluminium Wire with Hook
Chipping Hammer
Rotary Hammer
Drill Machine
Ladder
Cont..

## Slide 16
Come a Long
Pointed Iron Rod
Plastic Sheets
Mats (Dari) with Round Hole
Hook with Extension Rod
PPE
Stethoscope
Cont..

## Slide 17
B P Apparatus Digital
Oxygen Cylinder
50 ft. Oxygen Passing Pipe.
Thermometer Digital
Octoscope and Nasal Speculum
Torch
Pen Light
Cont..

## Slide 18
Laryngoscope
Cervical Colour
Splints
Dressing Gauze
Cotton Bundle
Cup Paper
Surgical Tape
Cont..

## Slide 19
Hand Towel
CPR Mask
Bag Valve Mask
Suction Unit with Accessories
Foldable Stretcher/Spine Board with Accessories
MFR Box etc
Cont..

## Slide 20: REVIEW
After the completion of lecture you learnt the followings.
What is Bore well.
Classification of Bore well.
Bore well-Death Trap
Rescue Methods/Techniques
Equipment/ Improvised Equipment

## Slide 21: ANY QUESTION ?

## Slide 22: EVALUATION
What is Bore Well ?
Name any one technique adopted by NDRF.

## Slide 23
THANK YOU