## Slide 1
PEER | CSSR | INDIA
PPT 4 -
LESSON 4
Structural Triage and
INSARAG Marking System
PPT 4-1
Photo Credit: Freepik
Presented By:- Sohel Lakhani. DC

## Slide 2
PEER | CSSR | INDIA
PPT 4 -
Upon completing this lesson, you will be able to:
OBJECTIVES
1
2
3
Define Sectorization, its identification and five ASR Levels.
List four categories of Worksite Triage.
List at least 8 factors to consider in worksite triage.

## Slide 3
PEER | CSSR | INDIA
PPT 4 -
Upon completing this lesson, you will be able to:
OBJECTIVES
Define the INSARAG marking system, list and describe 8 categories of INSARAG Marking System
4

## Slide 4: OCHA - UNO
UN OCHA serves as the INSARAG Secretariat of the INSARAG Steering Group.
Mandated to coordinate international assistance in disasters exceeding the capacity of the affected country.
UN OCHA works with all participants to assist the government of the affected country in an effort to ensure the most effective use of international resources.

## Slide 5
International Search and Rescue Advisory Group (INSARAG)
INSARAG is a global network of more than 80 countries and organizations under the United Nations umbrella.
INSARAG deals with urban search and rescue (USAR) related issues, aiming to establish minimum international standards for USAR teams in earthquake response
UN Resolution 46/182 from 19th Dec 1991

## Slide 6
INSARAG REGIONAL GROUPS

## Slide 7
UNDAC = United Nations Disaster Assessment and Coordination
UNDAC was created in 1993
It is designed to help the United Nations and governments of disaster-affected countries during the first phase of a sudden-onset emergency
UNDAC also assists in the coordination of incoming international relief at national level and/or at the site of the emergency.

## Slide 8
UNDAC teams can deploy at short notice (12-48 hours) anywhere in the world.
They are provided free of charge to the disaster-affected country,
They are deployed upon the request of the United Nations Resident or Humanitarian Coordinator and/or the affected Government.

## Slide 9
Specifically in response to earthquakes, UNDAC teams set up and manage the On-Site Operations Coordination Centre (OSOCC) to help & coordinate international Urban Search and Rescue (USAR) teams responding to the disaster.

## Slide 10
LEMA
LEMA (Local Emergency Management Authority) is the ultimate responsible authority for the overall command, coordination and management of the response operation.
LEMA can refer to national, regional or local authorities, or combinations thereof, which are collectively responsible for the disaster response operation.

## Slide 11
1. Reception / Departure Centre
At entry/exit points (e.g. airports) to assist airport authorities with registration of international relief actors and facilitate their arrival and departure in terms of provision of information updates and logistics and administration support

## Slide 12
PEER | CSSR | INDIA
PPT 4 -
Sectorization
In case of large scale events, affecting large area or numerous cities, or even more than one country, Sectorization is done to allow effective co-ordination of Search and Rescue efforts for better operational planning and effective deployment of search and rescue teams.

## Slide 13
PEER | CSSR | INDIA
PPT 4 -
Sector
identification
A simple lettering system is used to code each sector, like A, B, C, D and so on and a local name or description can also be added to ensure clarity.
e.g. Sector A, Kashmir etc.

## Slide 14
PEER | CSSR | INDIA
PPT 4 -
Sector
identification

## Slide 15
PEER | CSSR | INDIA
PPT 4 -
Sector Assessment
worksite Triage Category Flowchart

## Slide 16
PEER | CSSR | INDIA
PPT 4 -
Occupancy type
Type of structure
Factors in Worksite Triage
Condition of the structure
Mechanism of collapse
Day, date, and time of collapse

## Slide 17
PEER | CSSR | INDIA
PPT 4 -
Prior intelligence
Availability of resources
Factors in Worksite Triage
(Cont.)
Location of utility shut-offs
Possible presence of hazardous materials

## Slide 18
PEER | CSSR | INDIA
PPT 4 -
INSARAG Marking System
The International Search and Rescue Advisory Group (INSARAG) Marking System uses symbols to identify the condition of structures, the presence of hazards and the status of victims in a standardized, simple and clear fashion that can be understood by all local, national and international rescue personnel.
The INSARAG Marking System consists of three principle Marking elements, these being:
Worksite Marking
Victim Marking
Rapid Clearance Marking

## Slide 19
PEER | CSSR | INDIA
PPT 4 -
Clear Markings
All markings must be conspicuous and made using a high contrast, durable, fluorescent colour.

## Slide 20
PEER | CSSR | INDIA
PPT 4 -
Marking System Information Categories
1
2
3
General Area Marking
Structure Orientation
Cordon Markings
Worksite Marking
4

## Slide 21
PEER | CSSR | INDIA
PPT 4 -
Marking System Information Categories (Cont.)
5
6
7
Victim Marking
Rapid Clearance Marking (RCM)
Facilities and Vehicle Markings
Team and Function Markings
8

## Slide 22
PEER | CSSR | INDIA
PPT 4 -
General Area Marking
Street & Number Identification

## Slide 23
PEER | CSSR | INDIA
PPT 4 -
Location References — Exterior and Interior

## Slide 24
PEER | CSSR | INDIA
PPT 4 -
Identifying Floors

## Slide 25
PEER | CSSR | INDIA
PPT 4 -
Identifying Columns/ Pillars

## Slide 26
PEER | CSSR | INDIA
PPT 4 -
Operations Work Zone

## Slide 27
PEER | CSSR | INDIA
PPT 4 -
Collapse / Hazard Zone

## Slide 28: 1 M
PEER | CSSR | INDIA
PPT 4 -
1.2 M
Place the mark at
the primary access point into the structure.

## Slide 29
PEER | CSSR | INDIA
PPT 4 -
Marking Format

## Slide 30
PEER | CSSR | INDIA
PPT 4 -
Sample Marking:
“Work in Progress”

## Slide 31
PEER | CSSR | INDIA
PPT 4 -
Sample Marking:
“Work Completed”

## Slide 32
PEER | CSSR | INDIA
PPT 4 -
Sample Marking:
“Work Completed”

## Slide 33
PEER | CSSR | INDIA
PPT 4 -
Potential Victim Location
Draw a large “V” as close as possible to the location of known or potential victim(s).

## Slide 34
PEER | CSSR | INDIA
PPT 4 -
Confirmed
Live Victims

## Slide 35
PEER | CSSR | INDIA
PPT 4 -
Update of Victims

## Slide 36
PEER | CSSR | INDIA
PPT 4 -
Extricated
All Victims

## Slide 37
PEER | CSSR | INDIA
PPT 4 -
Rapid Clearance Marking (RCM)
Clear
Deceased

## Slide 38
PEER | CSSR | INDIA
PPT 4 -
Table Top Exercise

## Slide 39
PEER | CSSR | INDIA
PPT 4 -
Table Top Exercise

## Slide 40
THANK YOU

## Slide 41
PEER | CSSR | INDIA