## Slide 1
PROTECTION AGAINST RADIATION (TIME DISTANCE SHIELDING)
Presented By:- Amit Kumar, AC

## Slide 2
OBJECTIVES
Upon completion of this lesson you will be able to:
Radiation.
Types of Radiation hazard (Internal, External)
Describe effect of TDS.
Define HVL and TVL.
Conclusion

## Slide 3: CAN HUMAN BEINGS SENSE THE RADIATION?
No

## Slide 4: RADIATION
Transmission of energy as particles or as electromagnetic waves from the nucleus of an atom .
Radiation are two type
1 Ionizing Radiation
2 Non- Ionizing Radiation

## Slide 5: RADIATION

## Slide 6: TYPE OF RADIATION HAZARDS
Radiation hazards are broadly classified as:
External Radiation Hazard: External radiation hazards occur when the source of radiation is outside body .
Internal Radiation Hazard: Internal radiation hazards results when the body is contaminated internally with a radioisotope.

## Slide 7: PROTECTION AGAINST INTERNAL EXPOSURE
Use additional caution with potential sources of airborne radiation.
No eating, drinking, smoking in potentially contaminated areas .
Wear proper protective equipment.
Cover open wounds.
Perform frequent surveys.

## Slide 8: PATHWAYS OF INTERNAL EXPOSURE
Inhalation (Nose)
Ingestion (food & Water)
Injection (Through Cut And Wounds)

## Slide 9: IONIZING RADIATION

## Slide 10: ALPHA PARTICLE
Weight : Heavy
Range in air : < 5 cm
Charge : +2
Shielding : A sheet of paper
Hazard : Internal only

## Slide 11: BETA PARTICLE
Charge : -1
Weight : very light
Range in air : Energy dependent
Hazard : Both internal & external
Shielding : Low Z (ie Lucite , plastic)

## Slide 12: PENETRATION POWER OF RADIATION

## Slide 13: PENETRATION POWER OF RADIATION
Alpha
a
++
g
Beta
Gamma and X-rays
Neutron
Paper
Plastic
Lead
Concrete
n

## Slide 14: RADIATION PROTECTION TECHNIQUES
ALARA Principle
The three basic factors by which external radiation hazard can be controlled are :
Time
Distance
Shielding

## Slide 15: TIME
Time is used as a safety factor by keeping the time of exposure to a practical minimum to execute the work. The dose received by a individual for a given exposure time follows the simple equation.
Total Dose = Dose Rate x Exposure time
Thus, lesser the time spend near the radioactive source, lesser would be radiation dose.

## Slide 16: TIME RELATIONSHIP

## Slide 17: TIME MANAGEMENT
Minimize the time of exposure.
Any work with radiation source should be planned in advance.
Dummy operations should be carried out to familiarize the anticipated situations.
Work should be shared by the group/staff to minimize the individual dose.

## Slide 18: DISTANCE
The most effective and economical method of reducing external radiation hazard is to increase the distance between the radiation source and the person at work.
The intensity of radiation falls off by the square of distance from the source. This is known as inverse square law.

## Slide 19: DISTANCE EFFECT

## Slide 20: DISTANCE EFFECT
Mathematically it can be expressed as
R = k/D2
Where R-Rad. Dose, D- Distance from source
and k-constant for particular radioactive source.
As k is constant for particular source and if source is not changed then we have
I1D12 = I2D22
where,
I1 is the radiation intensity at distance D1
I2 is the radiation intensity at distance D2

## Slide 21: SHIELDING
When available maximum distance and minimum time do not bring the radiation to an acceptably low value.
Materials like concrete, steel, lead and other high Z materials are used as a shield, between x-ray or gamma radiation sources and personnel.
These shielding materials absorb the radiation.

## Slide 22: SUGGESTED SHIELDING MATERIALS
Alpha : Nil
Beta : plastic sheet, Perspex, Aluminum
Gamma : sand bags, bricks, steel, concrete, lead.
X-ray : concrete, lead
Neutron : water, concrete

## Slide 23: HVL & TVL
HVL - (Half value layer): -
Which reduces the intensity of radiation by one half of its initial value.
TVL (Tenth value layer): -
It is a thickness of a specified substance which reduces the intensity of radiation by one-tenth (1/10) of its initial value.

## Slide 24
REVIEW
Radiation.
Types of Radiation hazard (Internal, External)
Describe effect of TDS.
Define HVL and TVL.
Conclusion

## Slide 25
ANY QUESTION?

## Slide 26
EVALUATION
1. What is HVL?
Ans- It is the thickness of a specific material needed to reduce the intensity of radiation by one half of its initial value.
2. What is the full form of TDS?
Ans- Time Distance Shielding

## Slide 27
THANK YOU