## Slide 1
CONTAMINATION & DECONTAMINATION PROCEDURE
Presented By:- Amit Kumar, AC

## Slide 2
OBJECTIVES
Upon completion of this lesson you will be able to:
Contamination
Types of contamination
Concept of decontamination
Types of decontamination
Steps of decontamination
Decontamination of personnel, Vehicle & Equipment.

## Slide 3: INTRODUCTION
Occupational workers as well as general population may be exposed to radiation by various routes following an accidental release of radioactivity from nuclear facilities.
Minor sine contamination may occur from time to time in nuclear facilities, hospital or industrial, laboratories where unsealed radioisotopes are handled.

## Slide 4: CONTAMINATION
Contamination may be defined as undesired presence of material in amounts that may be harmful to health and safety of personnel.
Types of contamination-:
1. External Contamination
2. Internal Contamination
Occur due to-
1. Inhalation (Nose)
2. Ingestion (Food & Water)
3. Injection (through wounds)

## Slide 5: REQUIREMENTS OF DECONTAMINATION
  Rapid in action.
  Efficiency.
  Harmless to humans.
  Non-corrosive and washable with water.
  Stable during storage.
  Easy to handle.

## Slide 6: AIM OF DECONTAMINATION
  To reduce the number of casualties.
  To decrease the clinical effect of the CW agent.
  To make the area safe for resuming normal activity.
  Site selection for decontamination:
  Security
  Sufficient space for personal & vehicle
  Availability of water
  Drainage system
  Wind direction

## Slide 7: TYPES OF DECONTAMINATION PROCEDURE
  Depending on methods-
  Physical
  Chemical (most suited and favored method)
  Depending on subjects-
  Individual
  Area & material (equipment , vehicles)

## Slide 8: PHYSICAL METHOD
  Scooping/Scraping (with wooden stick, knife, brush etc.)
  Evaporation (with hot air steam)
  Dilution and washing (with water, soap water)
  Adsorption (with fuller earth, sand, active charcoal)
Advantages of Physical decontamination
Cheapest.
Used for all type CW agent.
Easily available.

## Slide 9: PERSONAL DECONTAMINATION KIT (PDK)
PDK-1- This is personnel Decon. Kit .
This handy sachet Contains 20g.activated adsorbent powder
Use for decon. of skin against CW agents .
It is effective for all type of CW Agents .
PDK-2 - This is also personnel decontamination kit similar to PDK-I
The adsorbent powder(80g)
Used to decontamination of clothing and equipment.

## Slide 10: CHEMICAL METHOD
Decontamination through chemical method is more reliable and effective as compared to physical methods.
Convert toxic CW agent into innocent ( harmless) product.
This method however needs special chemicals and trained personnel.
Most widely accepted reaction for detoxification of CW agents by chemical modification are
  Oxidation
  Hydrolysis

## Slide 11: OXIDATION
In this type of reaction substance gains oxygen or loses hydrogen. V agents & Sulphur Mustard are highly vulnerable to oxidation. Chloramines are effective against mustard and V agents but ineffective against G agent.
Commonly used oxidants are:-
Sodium hypo chloride(NaClO)
Bleaching powder(STB)
Calcium hypo chloride

## Slide 12: HYDROLYSIS
It is the reaction of water with an organic compound it is facilitated by the presence of bases, acids. G type nerve agents can be rapidly decomposed by hydrolysis.
Such decontaminants are:-
Caustic soda (NaOH)
Baking powder (NaHCO3)
Washing powder (Na2CO3)

## Slide 13: DS-2 DECONTAMINATION SOLUTION
Composition:
1) NaOH - 2%,
2) Ethylene glycol monomethyl
ether - 28%,
3) Diethylene triamine - 70%.

## Slide 14: CHARACTERISTICSOF DS-2 SOLUTION
  Widely used in contamination with blister & nerve agents
  Used for equipment/vehicle & area decontamination
  Non-corrosive to metals but damages paints and rubber leather and plastic materials.
  Within 30 min contact time neutralize all known toxic chemical agents

## Slide 15: DS-2 SOLUTION
  Merits of DS-2
  DS-2 Ready to use solution.
Long term storage stability.
Long operative temperature.
Demerits of DS-2
  Damages paints and plastics.

## Slide 16: WHERE DECON. HAS TO BE CARRIED OUT?
Personal
Equipment
Vehicles
Terrain

## Slide 17: 4 STEPS OF DECONT. FOR VICTIMS
Garments off
Showering
Monitoring
Re issue clothing /registration.

## Slide 18: PERSONNEL DECONTAMINATION

## Slide 19: STEPS OF PERSONNEL DECONTAMINATION
Individual gear drop.
Shuffle Pit.
Over garment off ( CBRN suit removal).
Over boots and gloves off.
Monitor.
Mask removal.
Showering.
Re-monitoring.
Re issue clothing / Registration.

## Slide 20: STEP 1 INDIVIDUAL GEAR DROP

## Slide 21: STEP 2 SHUFFLE PIT

## Slide 22: STEP 3 OVER GARMENT OFF

## Slide 23: STEP 4 OVER BOOTS AND GLOVES OFF

## Slide 24: STEP 5 MONITOR

## Slide 25: STEP 6 MASK REMOVAL

## Slide 26: STEP 7 SHOWRING

## Slide 27: STEP 8 RE- MONITORING

## Slide 28: STEP 9 RE-ISSUE CLOTHING/ REGISTRATION

## Slide 29: STEPS OF DECON. AT SITE

## Slide 30: LAYOUT OF DECON. STATION

## Slide 31: STEPS OF EQUIPMENTS DECONTAMINATION
Isolation and Segregation
Initial Survey
Removal of Loose Contamination
Decontamination
Monitoring and Survey
Repeat Decontamination, In cases of persistent or high levels of contamination
Equipment Inspection
Documentation
Release for Use

## Slide 32: EQUIPMENTS DECONT.
  Immediate decontamination of personal equipment and certain other kinds of smaller equipment is generally done with individual decontaminants.
  The decontamination of equipment is done by PDK-2.
  Equipment / material can be painted with chemical resistant paint system e.g. polyurethane paint.
  Other methods are utilizing heat, steam or hot air.

## Slide 33: VEHICLE DECONT.
Requires large water supplies.
Set up decontamination station close to water source.
Rescuers involved should wear non-permeable rubber suits.

## Slide 34: PHASES OF VEHICLE DECONT.
Pre treatment.
Main treatment (Tetrachloride Ethylene)
Reaction station (30 Min.)
Post treatment
Interior decontamination .
Monitoring.

## Slide 35: PRE- TREATMENT

## Slide 36: MAIN TREATMENT

## Slide 37: REACTION STATION

## Slide 38: POST TREATMENT

## Slide 39: INTERIOR DECONT.
Purpose: Decontamination of Crew Compartment and driver exchange point.
Procedure: Driver Opens all hatches, Personnel from Decontamination Team enters and wipes surfaces with hot water. Decontamination can be carried out with PDA, Decofog etc.
Requirements:
  Pers : One
  Mtrl : Hot Water/Steam

## Slide 40: INTERIOR DECONT.

## Slide 41: MONITORING
Purpose: tells whether significant contamination is present or not.
Procedure: Chem detector papers to blot various dry surfaces on vehicle/or use of RVD kit/cam.
Requirements
  Personnel: two,: one with chem detection other with radio meter. (Both from contaminated unit)
  Materials
    Chem detector paper.
    RVD
    Radio meter.

## Slide 42: MONITORING

## Slide 43: AREA DECONT.
Mop the area with soap solution – dry mop
the area
Check for any loose contamination
Mop with soap solution mixed with citric acid
If contamination remains - Chipping and re-plastering (Concrete)
- Acid cleaning
- Painting of surface ( low contamination)

## Slide 44: DECONTAMINATION ARRANGEMENTS
Trained decontamination team
Setup site for decontamination
Dressing and undressing team
Full protection gear
Hand held detection devices
Decontamination solution and devices
Communication devices
Transport

## Slide 45
REVIEW
Contamination
Types of contamination
Concept of decontamination
Types of decontamination
Steps of decontamination
Decontamination of personnel, Vehicle & Equipment.

## Slide 46
ANY QUESTION?

## Slide 47
EVALUATION
1. Weight of PDK-II
a) 80 mg
b) 20 gm
c) 80 gm
d) 20 mg
Ans- c) 80 gm
2. ------- % of Diethylene triamine in DS-2
a) 2 %
b) 28 %
c) 70 %
d) 72 %
Ans- c) 70%

## Slide 48
THANK YOU