## Slide 1
-
TOOLS, EQUIPMENT AND
ACCESSORIES
COLLAPSE STRUCTURE SEARCH & RESCUE
CAPF | CSSR| INDIA
Presented by:- Pavan Dev Gaur, 2IC

## Slide 2: OBJECTIVES
Define tools, equipment and accessories (TEA).
List four categories of TEA according to their use.
List five power sources for equipment and tools.
Upon completing of this lesson, you will be able to :-
1
2
3

## Slide 3
List the general steps for use and maintenance of tools and equipment (before, during and after their use).
Demonstrate in four practical exercises the correct use of TEA.
4
5
OBJECTIVES

## Slide 4: TOOLS
A TOOL IS A DEVICE THAT IS USED TO PERFORM OR FACILITATE MANUAL OR MECHANICAL WORK, USING ONLY THE STRENGTH OF THE OPERATOR.
Examples:
Crow Hammer
Hack Saw
Pick Mattock

## Slide 5
EQUIPMENT
A piece of equipment is a machine or device that performs a physical task, whose operation depends on an external power source in order to increase work capacity.
Chain Saw
Electric Drill
Chipping Hammer
Examples:

## Slide 6
An accessory is a component that supplements or completes a tool or piece of equipment, and which increases the operator’s ability to perform a task.
ACCESSORIES
Examples:
Drill Bit
Hack Saw Blade
Hack Saw Blade

## Slide 7
CLASSIFYING TOOLS, EQUIPMENT AND ACCESSORIES ACCORDING TO THEIR USE
1.Search TEA
Search tools, equipment and accessories are used in searching for potentially trapped victims and locating them in collapsed structures.
They can be used individually or in conjunction with each other.

## Slide 8
2.Rescue TEA
Rescue tools, equipment and accessories are those used to penetrate a structure and gain access to a victim in a CSSR operation.
CLASSIFYING TOOLS, EQUIPMENT AND ACCESSORIES ACCORDING TO THEIR USE

## Slide 9
3.Operations Support Equpt. and Accessories
This category includes all items and devices used to aid in conducting a CSSR operation and which support rescue activities.
CLASSIFYING TOOLS, EQUIPMENT AND ACCESSORIES ACCORDING TO THEIR USE

## Slide 10
4. Personal Protective Equipment
Personal Protective Equipment Personal protective equipment (PPE) is required in order to prevent injury while working on a CSSR operation. Some basic PPE items are:
CLASSIFYING TOOLS, EQUIPMENT AND ACCESSORIES ACCORDING TO THEIR USE

## Slide 11
1.Electrically-powered
Electric tools and equipment are used to cut, penetrate and break materials. Examples: circular saws, electric drills
CLASSIFYING TOOLS AND EQUIPMENT ACCORDING TO POWER SOURCE

## Slide 12
2.Pneumatic (Air-Powered)
Pneumatic tools and equipment use pressurized air to cut, hammer and lift. They can be powered by a motor-driven compressor or pressurized air cylinders.
Examples: pneumatic cutters, breaker hammer and air bag
CLASSIFYING TOOLS AND EQUIPMENT ACCORDING TO POWER SOURCE

## Slide 13
3.Internal Combustion
These tools use fuel-burning, 2-cycle or 4-cycle motors. These are most commonly cutting tools.
Examples: chainsaw, rotary rescue saw.
CLASSIFYING TOOLS AND EQUIPMENT ACCORDING TO POWER SOURCE

## Slide 14
4.Hydraulic
These tools use the same principle as pneumatic tools, using pressurized hydraulic fluids instead of air.
CLASSIFYING TOOLS AND EQUIPMENT ACCORDING TO POWER SOURCE

## Slide 15
5.Other Types
Some tools do not fall into any of the four categories mentioned above.
Examples of these include the acetylene torch, come-along, and multi cable winch.
CLASSIFYING TOOLS AND EQUIPMENT ACCORDING TO POWER SOURCE

## Slide 16
There are seven general steps you should follow when using any tool or piece of equipment in a CSSR operation.
These steps are in addition to the specific instructions for each particular tool or piece of equipment.
GENERAL STEPS FOR USE AND MAINTENANCE

## Slide 17
Before
Put on all required PPE.
Verify availability of fuel and power sources.
Verify proper operation of tool.
Check required accessories for each tool or piece of equipment.
Follow all safety rule (course rules and manufacturer’s rules)
GENERAL STEPS FOR USE AND MAINTENANCE

## Slide 18
During
Use proper technique when using a tool or piece of equipment.
After
Follow proper cleaning and maintenance procedures for each tool or piece of equipment.
GENERAL STEPS FOR USE AND MAINTENANCE

## Slide 19
Follow these important guidelines when using various pieces of equipment:
Always use the proper bit or blade for the material to be penetrated and make sure that it is firmly installed in the equipment before operating.
Do not operate a drill until it is in contact with the material to be penetrated
TIPS FOR USING EQUIPMENT

## Slide 20
Conversely, when operating a rotary saw, bring it up to full speed before making contact with the material to be penetrated.
When drilling, do not stop the drill while the bit is inside the material – doing so may cause the bit to jam in the material. Likewise, do not allow the blade of a rotary saw to come to a stop while cutting material – remove it fully first.
TIPS FOR USING EQUIPMENT

## Slide 21
If a drill bit becomes jammed in the material and you are unable to remove it with normal drill action, do not use the whole drill as a lever on the bit – remove the drill from the bit and try to loosen it with hand tools.
TIPS FOR USING EQUIPMENT

## Slide 22
The Equipment Monitoring Form on the following page is as a sample for tracking all activity and usage for a piece of equipment. The Maintenance Log and Use Log portions can be broken out onto separate pages, as those portions can become lengthy. Because the form records maintenance, it is essential from the safety standpoint.
EQUIPMENT MONITORING FORM

## Slide 23
EQUIPMENT MONITORING FORM

## Slide 24: REVIEW
Define tools, equipment and accessories (TEA).
List four categories of TEA according to their use.
List five power sources for equipment and tools.
Upon completing of this lesson, you are able to :-
1
2
3

## Slide 25: REVIEW
List the general steps for use and maintenance of tools and equipment (before, during and after their use).
Demonstrate in four practical exercises the correct use of TEA.
4
5
Upon completing of this lesson, you are able to :-

## Slide 26
ANYQUESTIONS ?

## Slide 27
THANK YOU